## Slide 1: Networking
Understanding Network Infrastructure

## Slide 2: Network Components
Data
Client
Server
Peer
Network adapter
Network Media
Network Devices

## Slide 3: Server vs Client
Server
  Computer that provides shared resources and serves client requests
Client
  Computer that sends requests to other computers in the network
3

## Slide 4: OSI vs TCP/IP

## Slide 5: OSI Model
1
Physical
Physical
2
Physical
Data-Link
3
Physical
Network
4
Transport
5
Session
6
Presentation
7
Application
Open Systems Interconnection model
Conceptual/Reference model
Defines generic network communication processes
Layers communicate (pass information) with the layers above and below them
Gives people “jargon” with which to talk about data processing over a network

## Slide 6: TCP/IP Model
Network Interface
Internet
Transport
Application
1
Physical
Physical
2
Physical
Data-Link
3
Network
4
Transport
5
Session
6
Presentation
7
Application
Transmission Control Protocol/Internet Protocol
Developed prior to the OSI model
Developed by Department of Defense (DoD) in 1960s
Based on standard protocols
The “de facto” standard

## Slide 7: Transport Protocols (Layer 4)
Transmission Control Protocol (TCP)
  Connection oriented
    Establish connection before data can be sent
    Uses Three-way handshake
  Reliable and Error-checked
    Error detection algorithm
    Order algorithm
User Datagram Protocol (UDP)
  Simple
    Minimum of protocol mechanisms
    Minimum latency
  Not connection oriented
    Good for applications that do not require reliable data stream service
    Application developers must implement reliability on application layer
But Wait! There is more…
  Stream Control Transmission Protocol (SCTP)
  Datagram Congestion Control Protocol (DCCP)

## Slide 8: Sockets and Ports
Combination of protocol, port number, source and destination IP address
Server
Destination IP
10.20.30.1
Listen on
Port
80
Client
Source IP
10.20.30.40
Source
Port
24381

## Slide 9: Well known application protocols
HTTP
SMTP
  SMTP Server to SMTP Server delivery
  SMTP Client to SMTP Server delivery
POP3
IMAP
DNS
DHCP
FTP
SSH
RDP
VNC
NTP

## Slide 10: IP Addressing

## Slide 11: What is an IP Address?
Internet Protocol Address
Numerical label
Each device in TCP/IP network has an IP address
Displayed in human-readable notation
  IPV4 - 172.16.254.1
  IPV6 - 2001:db8:0:1234:0:567:8:1 (human-readable :D)
IP versions
  IPV4
    32 bits
    First deployed in 1983 (ARPANET)
  IPV6
    128 bits
    First deployed in ~2000
  Today, we use both versions of the IP simultaneously

## Slide 12: IANA
Internet Assigned Numbers Authority (IANA)
  Global standardization organization (Located in US)
Oversees global IP address allocation
  IPV4 and IPV6
  IANA delegates allocations of IP address blocks to regional Internet registries
  Each RIR allocates addresses for a different area of the world
  IANA manages the global registry of the BGP Autonomous System Numbers (ASNs)
Manages the data in the root DNS nameservers
No more IPV4 public addresses…

## Slide 13: IPV4 Addresses
32 Bits
  11000000101010000001111000101000
4 groups of 8 bits (Octet)
  11000000.10101000.00011110.00101000
Decimal base
  192.168.30.40

## Slide 14: IPV4 Calculation
0
0
0
0
0
0
1
1
0
0
0
1
0
1
0
1
0
1
1
1
1
0
0
0
0
0
0
1
0
1
0
0
168
30
40
192
1*128 + 1*64
1*128 + 1* 32 + 1*8
1*16 + 1*8 + 1*4 + 1*2
1*32 + 1*8

## Slide 15: Subnet mask (IPV4)
Also known as netmask
Solves some of the problems of classful addressing
Consists of 32 bits
Sequence of ones (1) followed by a block of zeros (0)
  Ones - indicate bits used for the network prefix
  Zeros - designates the host identifier
CIDR alternate method of representing subnet mask
  Count of the number of network bits prefixed with “/” – 192.0.2.130/24
 | Binary form | Dot-decimal notation
IP Address | 11000000.00000000.00000010.10000010 | 192.0.2.130
Subnet mask | 11111111.11111111.11111111.00000000 | 255.255.255.0
Network prefix | 11000000.00000000.00000010.00000000 | 192.0.2.0
Host identifier | 00000000.00000000.00000000.10000010 | 0.0.0.130

## Slide 16: IPV6
128 bits
  0010000000000001000011011011100000000000000000000010111100111011 0000001010101010000000001111111111111110001010001001110001011010
8 groups of 16 bits
  0010000000000001 0000110110111000 0000000000000000 0010111100111011 0000001010101010 0000000011111111 1111111000101000 1001110001011010
HEX base 16 bits
  2001:0DB8:0000:2F3B:02AA:00FF:FE28:9C5A
Removing leading zeros
  2001:DB8:0:2F3B:2AA:FF:FE28:9C5A
No subnet mask
  Prefix Length or just prefix
  Similar to CIDR in IPV4
No broadcast

## Slide 17: DHCP
Dynamic Host Configuration Protocol
Dynamically assigns network configuration
Reducing the need for manual network administration
From home networks to big enterprise
DORA
Discover package is sent to every device in the network (Broadcast)
DHCP
Client
DHCP
Server
1. Discover
2. Offer
3. Request
4. Acknowledge

## Slide 18: DNS
Domain Name System
Hierarchical naming structure - www.my.website.example.com
Decentralized architecture
Essential component of the Internet
Main goal
  Translates human-readable domain names to the numerical IP addresses
Components
  Name servers
  Zones
  Resolvers
  Records
    A
    PTR
    CNAME
    MX
    NS
    More…

## Slide 19: Wired vs Wireless
IEEE
  IEEE 802.3 – Ethernet networks
  IEEE 802.11 – Wireless local area networks

## Slide 20: Network Adapter
Converts instructions from upper layers into
  Electrical signals
  Optical signals
  Wireless waves
Converts the received signals into meaningful data for the upper layers

## Slide 21: Hub and Switch
Hub
  You can find such devices in a museum
  Simple signal repeater
  Supports multiple ports
  Star wiring and central point of wiring
  Layer 1 device
Switch
  Same functions as Hub + more
  Intelligent signal repeater
    Understand the source and destination address
    Repeats signals only to proper destination ports
  Layer 2
  Some switches support Layer 3 and Layer 4 features
Enhanced Switch
  Router capabilities
  Firewall capabilities
  QoS

## Slide 22: VLAN
Network traffic isolation
Groups physical or virtual devices in a logical network
Flexible management
  No need to rewire network
  No need to move devices

## Slide 23: Router
Layer 3
Routes traffic between networks
Routes traffic based on routing table
Manages routing tables by routing protocols

## Slide 24: Routing Protocols
OSPF
BGP
IS-IS
IGRP
EIGRP
RIP

## Slide 25: Internet
The Internet is a system of interconnected networks that spans the globe

## Slide 26: Intranets and Extranets
Intranets are:
  A group of services hosted on a network
  A private structure
  Internet-like service provision
Extranets are:
  Similar services to Intranet
  Exposed to networks outside of the Intranet
  Services that require extra security measures

## Slide 27: Firewall
A firewall is used to protect a private network from security risks inherent to connecting to an untrusted network
Rule based filtering
Anti-Virtus (AV) based filtering

## Slide 28: IDS and IPS
Intrusion Detection System
  Monitoring the events occurring in your network
  Analyzing traffic for signatures that match known cyberattacks
  Analyzing traffic for anomalies
Intrusion Prevention System
  the process of performing intrusion detection and then stopping the detected incidents

## Slide 29: VPN
Virtual Private Network
Method of extending a private network across public networks
Encryption is a common part of VPN
VPN Consumers
  Remote users
  Mobile users
  Branch offices

## Slide 30: Proxy and Reverse Proxy Servers
Proxy servers
  Cache information
  Category based filtering
  Anti-Virtus (AV) based filtering
  Artificial Intelligent (AI) based filtering
  Auditing and logging
Reverse proxy servers
  Controlling web traffic
  Securing web traffic
    Offload HTTPS
    Inspect traffic
  Allow load balancing

## Slide 31: Load Balancer

## Slide 32: Web Services

## Slide 33: Web Services
The era before the Web Services
  Inter-process communication (IPC)
    Using pipes, shared memory, message queues, semaphores/mutex, COM, etc.
  Inter-process communication over network
    Using sockets, DCOM, RPC, CORBA, RMI, etc.
HTTP - the “de facto” web services transport protocol
  Exchange objects and messages through HTTP protocol
  Foundation of the World Wide Web
  Universally accepted
  Firewall friendly
  Secure (HTTPS)
  Variety of tools and languages

## Slide 34: SOAP and REST
SOAP
  Simple Object Access Protocol
  Strict rules to prepare request and response
  Web Services Description Language (WSDL)
  Relies heavily on XML
  “Legacy”
REST
  Representational State Transfer
  Not very restrictive
  Closer to Web in design philosophy
    URI based
    HTTP Verbs
    HTTP Status codes
  Variety of data formats (XML, JSON, YAML, etc)
  Foundation for Microservices

## Slide 35: SOAP Example
HTTP/1.1 200 OK
Date: Fri, 22 Nov 2013 21:09:44 GMT
Server: Apache/2.0.52 (Red Hat)
SOAPServer: SOAP::Lite/Perl/0.52
Content-Length: 566
Connection: close
Content-Type: text/xml; charset=utf-8
<?xml version="1.0" encoding="UTF-8"?>
<SOAP-ENV:Envelope xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"
xmlns:SOAP-ENC="http://schemas.xmlsoap.org/soap/encoding/"
xmlns:SOAP-ENV="http://schemas.xmlsoap.org/soap/envelope/"
xmlns:xsd="http://www.w3.org/2001/XMLSchema"
SOAP-ENV:encodingStyle="http://schemas.xmlsoap.org/soap/encoding/">
  <SOAP-ENV:Body>
    <namesp1:easter_dateResponse xmlns:namesp1="http://www.stgregorioschurchdc.org/Calendar">
    <s-gensym3 xsi:type="xsd:string">2014/04/20</s-gensym3>
    </namesp1:easter_dateResponse>
</SOAP-ENV:Body>
</SOAP-ENV:Envelope>

## Slide 36: REST Example
GET http://server/employees HTTP/1.1
Host: server
User-Agent: Client
HTTP/1.0 200 OK
Content-Type: application/json
Content-Length: 291
Access-Control-Allow-Origin: *
Server: Werkzeug/0.14.1 Python/3.6.7
Date: Thu, 28 Feb 2019 09:57:01 GMT
[
{
"id": 1,
"name": "John Doe",
"status": "enabled",
"lastAction": "enable",
"lastActionReason": "Hire new Python Developer."
},
{
"id": 2,
"name": "Doe Johnson",
"status": "disabled",
"lastAction": "disable",
"lastActionReason": "Left the company."
}
]